ESP32-S3-DevKit-LiPo
User Manual

Document revision 2.0, August 2024	www.olimex.com

# Introduction to ESP32-S3-DevKit-LiPo

ESP32-S3 is a dual-core XTensa LX7 MCU, capable of running at 240 MHz. Apart from its 512 KB of internal SRAM, it also comes with integrated 2.4 GHz, 802.11 b/g/n Wi-Fi and Bluetooth 5 (LE) connectivity that provides long-range support. It has 45 programmable GPIOs and supports a rich set of peripherals. ESP32-S3 supports larger, high-speed octal SPI flash, and PSRAM with configurable data and instruction cache.

The board has two variants: ESP32-S3-DevKit-Lipo comes with module with PCB antenna as seen in the picture on the first page, while ESP32-S3-DevKit-Lipo-EA comes with U.FL connector for external antenna.

ESP32-S3-DevKit-LiPo board is a development board with Espressif ESP32-S3 module and these features:

- ESP32-S3-WROOM-1-N8R8 8MB RAM 8MB flash
- Green status LED
- Yellow battery charge LED
- pUEXT 1.0 mm step connector
- USB-C for power supply and USB-serial programmer
- USB-C for OTG JTAG/serial connector
- LiPo battery charger
- LiPo battery connector
- External power sense
- Battery measurement
- Automatic power supply switch between USB and LiPo
- RESET button
- USER button
- Dimensions: (1.1×2.2)" ~ (27.94×55.88)mm

## Order codes for ESP32-S3-DevKit-Lipo and accessories:

ESP32-S3-DevKit-LiPo	ESP32-S3 development board with USB JTAG/debugger and LiPo	charger
USB-CABLE-A-TO-C-1M	USB-C power and programming cable
LiPo	A number of compatible batteries
UEXT	Extension modules and sensors
# HARDWARE
## ESP32-S3-DevKit-LiPo layout:

USB-C JTAG/OTG
USB-C UART
User Button
Status LED
ESP32-S3
pUEXT connector

LiPo battery connector
RESET
Charge LED

## ESP32-S3-DevKit-LiPo GPIOs:

POWER SUPPLY:

This board can be powered by:

+5V	EXT1.pin 21 can be input or output
USB-UART	USB-C connector
USB-OTG1	USB-C connector
LiPo battery
## ESP32-S3-DevKit-Lipo schematics:

ESP32-S3-DevKit-LiPo latest schematic is on GitHub

## UEXT connector:

UEXT connector stands for Universal EXTension connector and contain +3.3V, GND, I2C, SPI, UART signals.
UEXT connector can be in different shapes.
The original UEXT connector is 0.1” 2.54mm step boxed plastic connector. All signals are with 3.3V levels.

As the boards become smaller and smaller some smaller packages were introduced too beside the original UEXT connector
- mUEXT is 1.27 mm step boxed header connector which is with same layout as UEXT
- pUEXT is 1.0 mm single row connector (this is the connector used in RP2040-PICO30)
Olimex has developed number of MODULES with this connector. There are temperature, humidity, pressure, magnetic field, light sensors. Modules with LCDs, LED matrix, Relays, Bluetooth, Zigbee, WiFi, GSM, GPS, RFID, RTC, EKG, sensors and etc.

## pUEXT signals:

# SOFTWARE:

Olimex ESP32-S3-DevKit-LiPo has support in the ESP32 package for Arduino IDE. From the board selector there is entry “OLIMEX ESP32-S3-DevKit-Lipo”.

The module is also supported in ESP-IDF.

Additionally we’ve seen some customer project for booting Linux off the board:

- ESP32-S3-DevKit-Lipo Linux image
- ESP32-S3-DevKit-LiPo Linux build instructions from jcmvbkbc and here
ESP32-S3-DevKit-Lipo Linux build instructions form ESP32DE
# Revision History
Revision 1.0 July 2023
Revision 2.0 August 2024